SSU RMS
Last Updated: July 4, 2010

IK Algorithm
This calculates all joint angles given the EE position, direction and rot vectors.
Reference frame:
+X: Towards orbiter tail
+Y: Towards port side (right from aft windows)
+Z: Up
In the stowed position, the SP, EP and WP joints rotate around the Y-axis; the SY and WY joints rotate around the Z-axis; the WY joint rotates around the X-axis.

1. Subtract direction vector (multiplied by WY-EE distance) to get target WY joint.
2. All booms between shoulder joint and WY joint are in a plane. Calculate normal to boom plane.
3. SY angle is angle between boom plane and x-axis.
4. WY angle is complementary with angle between EE dir and normal to boom plane.
5. The WP_Normal vector is the cross product of the EE dir vector and the boom plane normal vector. The angle between the WP_Normal vector and the z-axis is the EE pitch angle (WP+EP+SP). If the WY angle is 90° (cross product is 0), the EE pitch angle is kept constant (i.e. The same as last timestep).
6. WR angle is the angle between the WP_Normal vector and the EE rot vector.
7. From WY position, boom plane and EE pitch angle, calculate target WP position.
8. SP joint (coordinate frame origin), EP joint and WP joint form a triangle where the lengths of all 3 sides are known. Use cosine law to calculate SP and EP angles.
9. Calculate the WP angle.

Calculating EE position
During single joint maneuvers, Orbiter's default calculations (rotation of VECTOR3 as part of the animation) is used to calculate the EE pos/dir/rot vectors. During IK maneuvers, the EE pos/dir/rot vectors are updated to the target values at each timestep. The position displayed on Panel A8 is always the value calculated by Orbiter.