The DPS ShuttleBus system

# Introduction

## The MDMs
### The SCU
The SCU is the controlling system of the MDM. It reacts to commands from the GPCs/PCMMUs and contains a 512 words Programmable Read-Only Memory (PROM), which permits automatic execution of I/O. The first sixteen words of the PROM are special and encode the types of installed hardware in the MDM.
### The MDM I/O cards
#### Type 1: Discrete input, low voltage
This input card reads digital signals in the range of 0 to 5V, 5V meaning high or true, 0V meaning low or false. It has 3 channels, each 16 bit channel being equal to 16 output lines.
#### Type 5: TACAN/Radar altimeter
This is a special kind of card, that combines serial I/O with analog I/O functions.

# MDMs
## Flight forward (FF) MDMs
All four flight forward MDMs can be interchanged and thus, use equal I/O hardware and equal PROM images.
### Bus control element numbers
MDM	BCE Number
FF1	10
FF2	11
FF3	12
FF4	13

### PROM Programs

FCINPUT1 – read 20 words (CW: 01011 0 0010 000010000 10011)
Call: ExecutePROM(bce, 16, 20, data);
Program:
FCINPUT1 EQU *
#READ 14,6,1
#READ 14,7,1
#READ 14,1,1
#READ 1,6,1
#READ 1,7,1
#READ 1,1,1
#READ 14,5,1
#READ 1,5,1
#READ 14,3,1
#READ 1,3,1
#READ 7,1,1
#READ 4,0,1
#READ 4,1,1
#READ 4,2,1
#READ 12,0,1
#READ 12,1,1
#READ 6,0,1
#READ 15,0,1
#READ 14,0,1
#READ 14,2,1

FCINPUT2 – multiple read operations
CW:
Call:
ExecutePROM(bce, 27, 7, data);	//01011 0 0010 000011011 00110
ExecutePROM(bce, 42, 8, data);	//01011 0 0010 000101010 00111
ExecutePROM(bce, 50, 1, data);	//01011 0 0010 000110010 00000
ExecutePROM(bce, 52, 1, data);	//01011 0 0010 000110100 00000
ExecutePROM(bce, 51, 1, data);	//01011 0 0010 000110011 00000

Program (remarks for FF1):
FCINPUT21 EQU *
#READ 4,0,1
#READ 4,1,1
#READ 4,2,1
#READ 12,0,1
#READ 12,1,1
#READ 6,0,1
#READ 15,0,1

FCINPUT22 EQU *
#READ 7,0,1	Fwd Attach Pt Cap Volts A
#READ 0,0,1	TACAN 1 Bearing Word A
#READ 0,1,1	TACAN 1 Bearing Word B
#READ 0,2,1	TACAN 1 Range Word A
#READ 0,3,1	TACAN 1 Range Word B
#READ 0,4,1	RADAR Alt 1 Parent Word
#READ 0,5,1	MDM FF1 Discrete in
#READ 0,6,1	MDM FF1 Discrete in
FCINPUT23 EQU *
#READ 11,1,6	ADTA 1
FCINPUT25 EQU *
#READ 11,0,14	IMU 1
FCINPUT24 EQU *
#READ 3,0,3	MSBLS 1

### I/O cards

Module address	Card type
0	TACAN/RALT
1	Analog input, differential
2	Discrete output
3	Serial I/O
4	Discrete input
5	Discrete output
6	Discrete input
7	Analog input
8	Analog output
10	Discrete output
11	Serial I/O
13	Discrete output
14	Analog input, differential
15	Discrete input

### Card 1 – Analog input
Channel address	Subsystem	Quantity
0
1	LH RHC	LH RHC CMD (A, B, C, D) Yaw
2
3	LH RPTA	LH RPTA CMD (A, B, C, D)
4
5	LH SBTC	LH SBTC CMD (A, B, C, D)
6	LH RHC	LH RHC CMD (A,B, C, D) Roll
7	RH RHC	RH RHC CMD (A, B, C, D) Pitch

### Card 3 – Serial I/O
Channel address	Subsystem	Quantity
0
1	MTU	Serial I/O
2

### Card 11 – Serial I/O
Channel Address	Subsystem	Quantity
0	IMU	Serial I/O
1	ADTA	Serial I/O
2

### Card 14 – Analog input
Channel Address	Subsystem	Quantity
0	AA	Norm Acc 1 signal
1	RH RHC	RH RHC CMD (A, B, C, D) Yaw
2	AA	Lat Acc 1 signal
3	RH RPTA	RH RPTA CMD (A, B, C, D)
4
5	RH SBTC	RH SBTC CMD (A, B, C, D)
6	RH RHC	RH RHC CMD (A, B, C, D) Roll
7	RH RHC	RH RHC CMD (A, B, C, D) Pitch

# MMU
BCE 18/19
Opcode 1 = Write with checksum
Opcode 2 = Write without checksum
Opcode 3 = Read with checksum
Opcode 4 =Read without checksum
Opcode 5 = MM Utility write